## Slide 1: MANAGEMENT OF CORONARY CALCIUM
Dr. Akif Baig
SCAI Expert Consensus Statement on the Management of Calcified Coronary Lesions. Journal of the Society for Cardiovascular Angiography & Interventions. 2023;3:101259

## Slide 2
Rising comorbidities have increased coronary artery calcification (CAC) and its association with obstructive coronary artery disease (CAD)
PCI in calcified CAD has lower procedural success and higher early and late complication rates.
Coronary calcification can:
  Impede stent delivery and deployment
  Cause stent underexpansion and malapposition
  Lead to direct stent damage

## Slide 3
Intravascular imaging (e.g., IVUS/OCT) is increasingly used to:
  Define the extent, type, and location of calcium
  Guide calcium modification strategies
  Improve optimal stent deployment and reduce adverse events

## Slide 4: Coronary Artery Calcification (CAC)
CAC develops alongside atherosclerosis and shares common pathophysiology.
Prevalence increases with age, starting in middle age; most individuals ≥80 years have CAC.
Major risk factors for CAC include:
  Chronic kidney disease
  Diabetes mellitus
  Hypertension
  Tobacco use
  High body mass index
  Inflammation
  Family history of heart disease

## Slide 5
CAC shows heterogeneous patterns, ranging from:
  Flow-limiting obstructive stenoses
  Partially obstructive or non-obstructive lesions confined to the vessel wall
  Lesions with or without positive remodeling

## Slide 7
Calcification may:
  Replace the intimal layer
  Develop subintimally
Based on stage and biology, CAC can appear as:
  Microcalcification (often linked to unstable plaques)
  Fibrocalcification
  Thick or thin calcific sheets, concentric or eccentric
Hydroxyapatite crystals may aggregate to form calcified nodules, with or without a fibrous cap

## Slide 8: Identification of calcified coronary lesions
Preprocedural identification
  CAC can be detected on noninvasive CT scans done for cardiac or noncardiac indications.
  CT provides useful information on location and extent of CAC, even without Agatston scoring or dedicated coronary CTA.

## Slide 9
Intraprocedural identification
  CAC may be detected using fluoroscopy or intravascular imaging.
  Fluoroscopy accuracy depends on calcium arc, length, and thickness.
  Sensitivity ~50% and specificity ~95% vs intravascular imaging.
  Limitations of fluoroscopy:
    Poor resolution for CAC subtype
    May overestimate calcium in some cases

## Slide 10
Role of intravascular imaging (IVUS/OCT)
  Improves detection and characterization of CAC.
  Defines:
    Calcium phenotype (nodules vs sheet calcium)
    Superficial vs deep wall calcium
    Arc, length, and thickness
  Associated with better clinical outcomes in complex PCI.

## Slide 11
Guideline recommendations
ACC/AHA/SCAI 2021 Revascularization Guidelines:
  IVUS: Class IIa, LOE B-R for procedural guidance, especially in left main/complex PCI.
  OCT: Reasonable alternative to IVUS, except in ostial left main disease.

## Slide 12: Imaging characteristics
IVUS: Bright echoes with acoustic shadowing.
OCT: Low backscatter, low attenuation, sharp borders.
Both IVUS and OCT measure arc and length.
Only OCT can accurately measure calcium thickness.
OCT has higher resolution but:
  Limited penetration depth
  Requires blood clearance

## Slide 14: IVUS-based morphologic predictors (calcified coronary lesions)
IVUS parameter | Threshold / Feature | Clinical significance
Calcium arc | 360° circumferential calcium | Greater stent expansion (>70%) with calcium modification
Calcium arc + length | >270° arc with calcium length ≥5.0 mm | Improved stent expansion after calcium modification
Vessel diameter | <3.5 mm | Higher benefit from calcium modification to achieve optimal expansion
Calcified nodules (CN) | Presence of CN | Associated with improved stent expansion when modified

## Slide 15: OCT-based morphologic predictors (calcified coronary lesions)
OCT parameter | Threshold / Feature | Clinical significance
Maximum calcium angle | Larger angle | Independent predictor of stent underexpansion
Calcium length | Longer length | Independent predictor of stent underexpansion
Calcium thickness | Increased thickness | Independent predictor of stent underexpansion
Calcium thickness (post-modification) | <0.5 mm | Higher likelihood of calcium fracture after modification

## Slide 16
Riley RF, Patel MP, Abbott JD, Bangalore S, Brilakis ES, Croce KJ, et al. SCAI Expert Consensus Statement on the Management of Calcified Coronary Lesions. Journal of the Society for Cardiovascular Angiography & Interventions. 2023;3:101259. doi:10.1016/j.jscai.2023.101259

## Slide 17
Calcified Nodules (CNs)

## Slide 18
Definition:
  CN is a convex calcium mass protruding into the lumen, overlying a severely calcified plate.
  May be eruptive, with fibrous cap disruption and luminal thrombus.

## Slide 20
Angiographic appearance:
  Large CNs can appear as radiolucent masses, mimicking thrombus.
Prevalence:
  Rare in general obstructive CAD (<5%).
  Much more common (~32%) in severely calcified lesions (maximum calcium angle >270°).

## Slide 21
Common locations & associations:
  Occur at hinge-motion segments of coronary arteries.
  More frequent in the right coronary artery (RCA).
  Higher prevalence in patients on chronic hemodialysis.

## Slide 22
Clinical impact:
  Presence of CN during PCI is linked to higher long-term MACE compared with calcified lesions without CNs.
  Early restenosis often due to reprotrusion of the CN into the stent.

## Slide 23
Imaging characteristics:
  OCT: Differentiates eruptive CNs (irregular surface) from noneruptive CNs (smooth fibrous cap).
  IVUS: Can identify CN shape and surface irregularity but has lower resolution and depth than OCT.

## Slide 24
Prognosis:
  Eruptive CNs show worse long-term outcomes despite better acute stent expansion, likely due to higher risk of reprotrusion.

## Slide 25: Long calcified lesions
Often associated with diffuse CAD and long-standing/uncontrolled risk factors.
Linked to higher long-term adverse cardiovascular events.
Longer calcium segments increase the risk of stent underexpansion during PCI.
Stenosis and severe calcification may not co-localize in long lesions.
Intravascular imaging is essential to:
  Precisely localize severely calcified segments
  Target calcium modification to areas at highest risk of underexpansion

## Slide 26: Chronic total occlusion (CTO) interventions
PCI of calcified CTOs has:
  Lower procedural success
  Higher complication rates than noncalcified CTOs
Preprocedural chest CT and intravascular imaging help:
  Define calcium distribution and morphology
  Guide strategy selection

## Slide 27
Proximal cap calcification reduces antegrade wiring success; may be identified via side-branch imaging.
During retrograde CTO techniques, intravascular imaging helps:
  Identify less calcified reentry zones
  Improve retrograde guidewire reentry success

## Slide 28: In-stent restenosis (ISR)
Defined as ≥50% stenosis within the stent on follow-up angiography.
Calcium-related ISR mechanisms:
  Initial stent underexpansion due to underlying calcification
  Calcified neoatherosclerosis within the stent

## Slide 29
Prevalence of calcified neoatherosclerosis:
  ~10% at 5–7 years
  ~20% beyond 7 years after DES implantation
Imaging predictors of repeat underexpansion:
  Large calcium arc (>180°)
  Thick calcium (>0.5 mm) within or adjacent to the stent

## Slide 30: Post–coronary artery bypass surgery (CABG)
Patients with severe coronary calcification have similarly high long-term mortality with PCI or CABG.
Most studies show accelerated atherosclerosis progression in grafted vessels.
Intravascular imaging reveals that native vessels proximal to graft anastomoses show:
  More severe calcification
  Higher prevalence of calcified nodules
  Greater negative remodeling compared with patients without prior CABG

## Slide 31
TREATMENT MODALITIES FOR
CALCIFIED CAD

## Slide 32: Semicompliant (SC) and Noncompliant (NC) balloons
Used for:
  Mildly calcified lesions
  Initial preparation of more severe calcification
Mechanism:
  Do not remove calcium
  Create medial dissections and disrupt thin calcium to increase plaque elasticity
Limitations in calcified lesions:
  Eccentric balloon expansion → risk of perforation or flow-limiting dissection
  “Watermelon-seeding” toward non-diseased segments
  Nonuniform expansion → balloon rupture, uncontrolled dissection, or perforation

## Slide 33: Cutting balloons (CB)
Less compliant balloons with microsurgical blades
Mechanism:
  Create controlled incisions
  Fracture calcium and improve symmetric stent expansion
  Reduce balloon slippage
COPS trial:
  CB vs NC balloon in severe CAC
  Higher minimum stent area (MSA) at calcium site with CB (8.2 vs 7.3 mm²; P = 0.035)
  No difference in final MSA
Wolverine CB:
  Lower-profile design
  Improved deliverability vs older CBs

## Slide 34: Scoring balloons
Designed for better deliverability and less vessel trauma than CBs
Comparative data:
  Wolverine CB more deliverable than Lacrosse NSE ALPHA
  Similar cross-sectional area gain
Available scoring balloons:
  AngioSculpt: SC balloon with 3–4 helical nitinol scoring elements
  Chocolate XD: SC balloon with nitinol cage creating pillows and grooves to control dissections
  Scoreflex NC: NC balloon with integrated nitinol wire; guidewire acts as second scoring element

## Slide 35: High-pressure balloons (OPN balloon)
Double-layer balloon capable of very high pressures
Study findings (326 undilatable lesions):
  53% yielded at 30–40 atm
  47% required >40 atm
  Angiographic success: 97.5%
  Procedural success: 96.6%
  Vessel perforation occurred in 3 patients
Technical recommendations:
  Predilation: undersize by 0.5 mm
  Postdilation: 1:1 sizing
Limitations:
  Higher risk of perforation, especially pre-stenting
  Balloon increases in size at high pressure
  Bulky profile and stiffness → difficult re-crossing

## Slide 36: Balloon-based treatment modalities for calcified CAD
Balloon type | Examples | Mechanism of action | Indications | Advantages | Limitations / Risks
Semicompliant (SC) balloons | Standard SC balloons | Expand with vessel compliance; create minor dissections | Mild calcification; initial lesion preparation | Easy deliverability; widely available | Eccentric expansion, watermelon seeding, limited efficacy in severe CAC
Noncompliant (NC) balloons | Standard NC balloons | High-pressure dilation; disrupt thin calcium | Mild–moderate CAC; post-modification optimization | Controlled sizing; high-pressure capability (20–24 atm) | Risk of perforation, uncontrolled dissection, balloon rupture in severe CAC
Cutting balloons (CB) | Wolverine CB (Boston Scientific) | Microsurgical blades create controlled incisions and calcium fractures | Severe CAC for plaque modification | Predictable dissection planes; less slippage; improved MSA at calcium site | Higher perforation risk; not for full lesion dilation alone
Scoring balloons | AngioSculpt, Chocolate XD, Scoreflex NC | External scoring elements focus force on plaque | Moderate CAC; ostial lesions | Better deliverability; reduced slippage; controlled dissections | Limited efficacy in deep or circumferential calcium
High-pressure balloons | OPN balloon (SIS Medical) | Double-layer balloon allows ultra–high-pressure dilation | Undilatable lesions resistant to NC balloons | Very high angiographic and procedural success | Increased perforation risk; balloon growth at high pressure; difficult re-crossing

## Slide 37
ROTATIONAL
ATHERECTOMY

## Slide 38: Burr sizing
Recommended burr-to-artery ratio: 0.4–0.6
1.5-mm burr for arteries ≤3.0 mm
1.75-mm burr for arteries >3.0 mm
Avoid 1.25-mm burr as first burr due to higher entrapment risk

## Slide 39: Guide catheter selection
1.25–1.5 mm burr → 6F guide
1.75 mm burr → large 6F (0.071”) or 7F guide
2.0 mm burr → large 7F (0.081”) or 8F guide
2.15 mm burr → 8F guide

## Slide 40: Guide wire considerations
RotaWire types: floppy and extra support
  Floppy wire: less vessel straightening, reduced wire bias, easier ablation in tortuous segments
  Extra support wire: better deliverability and eccentric plaque modification, but higher perforation risk
Primary wiring with RotaWire is often feasible

## Slide 41: Wire and burr safety
Keep distal RotaWire tip visible
Maintain ≥5 mm distance between burr and radiopaque wire segment
Reposition wire between runs to prevent wire fracture

## Slide 42: Lubrication and flushing
Use continuous RotaGlide infusion to reduce friction and heat
Avoid RotaGlide in patients with egg or olive oil allergy
Alternative: saline + heparin ± vasodilators (nitroglycerin/verapamil)

## Slide 43: Ablation technique
Use short, pecking motions
Each run <30 seconds
Avoid burr deceleration >5000 rpm
Perform a final polishing run with minimal resistance

## Slide 44: Troubleshooting uncrossable lesions
Increase rotational speed
Downsize burr
Improve guide support or use guide catheter extension
Extension requirements:
  1.25 mm burr → 7F extension
  1.5–1.75 mm burr → 8F extension
  2.0 mm burr → not compatible with extensions

## Slide 45: Temporary pacing
Usually not required with small burrs
Consider in patients with baseline conduction disease or low LV reserve, especially during RA of dominant RCA or circumflex

## Slide 46
The 2021 ACC/AHA/SCAI Coronary Artery Revascularization guidelines gave a 2a, level of evidence B-R, recommendation for the use of RA in patients with heavily calcified lesions, noting that RA “can be useful to improve procedural success.

## Slide 47: ORBITAL ATHERECTOMY
Guide catheter requirements
  Minimum 6F guide catheter
  7F system recommended if a guide extension is planned
Guide wire selection
  Primary wiring usually feasible with ViperWire Advance
  FlexTip option: 0.012″ nitinol core with 0.014″ tip
Wire safety
  Keep distal ViperWire tip in view
  Maintain ≥5 mm distance between wire tip and OA drive shaft to avoid wire fracture

## Slide 48
Vasodilator use
  Administer nitroglycerin before the first run and intermittently
  Helps minimize slow flow, as tolerated hemodynamically
Ablation technique
  Use smooth forward or backward motion at ~1.0 mm/s
  Slower motion and more runs correlate with greater lumen gain
  Never use force
  Ensure 1:1 motion between crown and advancer knob; if movement stops, do not push
Rotational speed
  Start at 80,000 rpm in all vessels
  Increase to 120,000 rpm in vessels ≥3.0 mm for larger lumen gain

## Slide 49
Run duration and total time
  Individual runs ≤30 seconds
  Total treatment time with same crown ≤5 minutes
Rest periods
  Rest time between runs should be at least equal to treatment time
  Rest in a nonocclusive position within the vessel
Conduction disturbances
  Transient conduction issues may occur in dominant RCA or circumflex
  Consider prophylactic aminophylline or temporary pacing when appropriate
Ostial lesion caution
  OA at ostial lesions carries risk of aortic dissection
  May be performed cautiously by experienced operators using distal positioning and retrograde activation, avoiding unrestricted crown orbit at the ostium

## Slide 50: Excimer Laser Coronary Atherectomy (ELCA)
Energy settings
  Although low settings are recommended by manufacturers, maximum settings are commonly used for calcified lesions
  Typical setting for 0.9-mm catheter: 80 mJ/mm² at 80 Hz
  Higher fluence increases vapor bubble size and calcium modification
Catheter sizing
  Choose catheter diameter ≈ two-thirds of the vessel diameter
Advancement technique
  Advance catheter slowly (<1.0 mm/s) to maximize time-dependent ablation

## Slide 51
Direction of laser use
  Forward-only motion for tissue ablation (uses front-facing energy)
  Bidirectional motion to improve lesion compliance via acoustic mechanical effects
Perforation prevention
  Continuously monitor nose cone orientation
  If catheter stalls and deflects, stop—laser may be directed toward the adventitia
Contrast-assisted laser (off-label)
  Contrast injection during laser activation increases cavitation and calcium fracture
  Useful for in-stent underexpansion due to calcium
  Carries higher risk of no-reflow and perforation

## Slide 52
Device-related complications
  Rare risk of distal radiopaque marker band separation with contrast use
Guide wire caution
  Avoid ELCA on polymer-jacketed guide wires due to risk of polymer damage

## Slide 53: Consensus tips for Intravascular Lithotripsy (IVL)
Best lesion type
  Most effective for circumferential calcium in balloon-crossable lesions
  Effective in eccentric and nodular calcium, but may require more pulses
Combination strategies
  Can be used synergistically with atherectomy
  Particularly useful in long lesions with heterogeneous vessel size and calcium pattern

## Slide 54
Hemodynamic considerations
  Use longer rest periods between pulse deliveries to reduce hemodynamic compromise
  Especially important in lesions supplying large myocardial territories (e.g., left main)
Guide wire compatibility
  Safe to use with multiple guide wires in place
  Advantageous in bifurcation lesions
Role of intravascular imaging
  Imaging helps identify optimal pulse locations, especially in long lesions
  Useful post-atherectomy, as atherectomy often modifies calcium in smaller vessel segments but may be less effective in larger segments

## Slide 55: Consensus tips for Calcified Nodules (CNs)
Role of intracoronary imaging
  Essential to define CN location, overall calcium distribution, and guide-wire bias
  Helps determine reference vessel size and select the optimal calcium-modification device
Orbital atherectomy (OA) strategy
  Use slow crown motion (~1 mm/s)
  Perform a high number of passes (>5)
  Prefer higher speed (120,000 rpm) for effective CN modification

## Slide 56
Rotational atherectomy (RA) strategy
  Improve burr contact by:
    Increasing burr-to-artery ratio to 0.6–0.7 in large lumens
    Using RotaWire Extra Support to correct unfavorable wire bias
Intravascular lithotripsy (IVL) strategy
  Size IVL balloon 1:1 with reference vessel diameter
  Expect need for more pulses compared with non-CN lesions
Pre-stenting optimization
  Perform 1:1 noncompliant (NC) balloon dilation
  Prefer repeat intravascular imaging to confirm calcium fracture before stent deployment

## Slide 57: Consensus tips for Chronic Total Occlusions (CTOs)
Intraplaque crossing + device-uncrossable lesions
  Bury a microcatheter in the proximal cap and exchange to a RotaWire
  Rotational atherectomy (RA) preferred over OA due to risks of orbital motion in dissection planes
  If dissections are present, use a 1.5-mm RA burr (forward ablative tracking; lower perforation risk than larger burrs)
When RotaWire exchange is not feasible
  Consider excimer laser coronary atherectomy (ELCA) with a 0.9-mm catheter at 80/80 settings
  Off-label contrast-assisted ELCA may be required for in-stent undilatable calcified lesions

## Slide 58
Intraplaque crossing + balloon-crossable lesions
  Perform initial balloon predilatation
  Choose the calcium-modification device based on intravascular imaging findings
Extraplaque crossing with residual calcium
  If balloon angioplasty is suboptimal, consider intravascular lithotripsy (IVL)
  RA may be used, but published experience is limited

## Slide 59: Consensus tips for In-Stent Restenosis (ISR)
Initial assessment
  Perform intravascular imaging (IVUS/OCT) whenever feasible to identify:
    Mechanism of stent failure
    Distribution of calcium (calcified neoatherosclerosis vs calcium behind stent struts)
Calcified neoatherosclerosis
  Treat similar to de novo calcified lesions:
    1:1 sized NC balloon
    Cutting or scoring balloon, followed by 1:1 NC balloon
    High-pressure balloon (undersized by 0.5 mm)
    Atherectomy or IVL (1:1 sizing) as needed

## Slide 60
Calcium behind stent struts with stent underexpansion
  Consider:
    Off-label IVL (1:1 sizing)
    High-pressure balloon (undersized by 0.5 mm)
    ELCA with off-label contrast
    Atherectomy (RA with burr-to-artery ratio >0.5)
Balloon-uncrossable ISR lesions
  Use ELCA (0.9-mm catheter) or RA (0.5 burr-to-artery ratio)

## Slide 61: Consensus tips for Aorto-ostial lesions
Balloon-crossable lesions
  Use cutting or scoring balloons
  Consider high-pressure balloons
  Intravascular lithotripsy (IVL) is an effective option for lesion preparation
Balloon-uncrossable lesions
  Proceed with atherectomy

## Slide 62
Rotational atherectomy (RA)
  Use burr-to-artery ratio ~0.5
  Ensure coaxial guide catheter support
  Consider upsizing guide catheter by +1F to reduce risk of guide catheter ablation
Orbital atherectomy (OA)
  Associated with risk of aortic dissection in ostial lesions
  May be used cautiously by experienced operators
  Advance device distal to lesion with glide assist
  Activate retrogradely, avoiding unrestricted crown orbit at the ostium